## Slide 1
🚲
bikestation.
The user journey of the Smart Bikestation
From finding a free spot to picking up the bike – and what happens if someone tries to steal it.
HACKATHON 2026
WORKING PROTOTYPE
Live demo: Stellplatz 1 · Hackathon Halle

## Slide 2
CONTEXT
Who is this for?
Three people interact with the station. The journey is designed around what each of them needs in the moment.
Cyclist
Student or commuter with a valuable bike or e-bike.
Needs: know if a spot is free before arriving · lock the bike without a key · be told immediately if something happens.
Admin / operator
Runs the station (school, city, company).
Needs: see who is at which box · react to alarms · add or remove stations · a clear log of events.
Station
Raspberry Pi 5 with ultrasonic sensor, servo latch and LED.
Needs: a simple rule – measure, report, move the latch as the server says.
Smart Bikestation · User journey
2

## Slide 3
THE JOURNEY
Five steps from free spot to pick-up
Every step is one click for the cyclist. The server decides, the station executes.
1
See a free spot
Overview shows "Stellplatz 1 is free" with its location.
2
Book
One click – the servo latch opens the box.
LATCH OPEN
3
Park
Ultrasonic detects the bike; after 5 s the box locks.
LATCH CLOSED
4
Pick up
Tap "Pick up" – the box opens again.
LATCH OPEN
5
Done
Bike removed for 5 s – box closes and is free again.
LATCH CLOSED
And if the bike leaves the locked box without being opened? The owner gets an alarm with sound, the box is blocked and the admin sees exactly who, when and where.
Smart Bikestation · User journey
3

## Slide 4
STEP 1 + 2
Find a free spot and book it
No app store, no key: the web app works on any phone or laptop.
WHAT THE CYCLIST DOES
Opens the site and sees "Stellplatz 1 is free" with location.
Taps the spot – lands on the booking page with the box highlighted.
Signs in (username + password only) and taps "Book".
The box opens in front of them.
Stellplatz 1 is free
Hackathon Halle
Book now
BEHIND THE SCENES
→
Overview refreshes every 3 s from GET /api/slots.
→
POST /api/boxes/1/book (JWT) – only if the station is online and the user has no other box.
→
Box state: Free → OpenForParking, a BoxEvent "Booked" is logged.
→
The Pi's next reading gets lockOpen: true – servo turns to 90°.
Smart Bikestation · User journey
4

## Slide 5
STEP 3
Park – the box locks itself
Detection is debounced so a hand or a single bad reading never locks the box.
WHAT THE CYCLIST DOES
Pushes the bike into the box.
Waits a moment – nothing else to do.
Sees "Your bike is safely locked" on their phone.
Green LED on the station goes off.
Locked
Your bike is safe
Pick up
BEHIND THE SCENES
→
Pi measures distance every second (HC-SR04) and POSTs it.
→
Bike ≤ 7 cm for 5 s → OpenForParking → Locked.
→
Answer lockOpen: false – servo moves in 10 soft steps to 45°.
→
If no bike arrives within 120 s the booking is released.
Smart Bikestation · User journey
5

## Slide 6
STEP 4 + 5
Pick up and leave
The box only opens for its owner – and closes again by itself.
WHAT THE CYCLIST DOES
Taps "Pick up" in the app.
The box opens, the bike comes out.
Walks away – the box closes and is free for the next person.
History shows the completed parking.
Stellplatz 1
Open for pickup
Opening...
BEHIND THE SCENES
→
POST /api/boxes/1/pickup – only the owner, only when Locked.
→
Locked → OpenForPickup, lockOpen: true.
→
Bike gone for 5 s → Free, parking ended "Completed".
→
Not taken within 120 s → locks again (bike stays safe).
Smart Bikestation · User journey
6

## Slide 7
WHEN SOMETHING GOES WRONG
The alarm journey
The bike disappears from a locked box without the owner opening it.
1
Bike removed
Station reports "nothing there" while the box is Locked.
›
2
3 s confirmed
Server: Locked → Blocked, parking ended "BikeRemoved", critical alert.
›
3
Owner alerted
Red banner on every page, repeating chime, vibration, blinking tab.
›
4
Admin reacts
Sees the alarm, the user and the time; checks the station on site.
›
5
Released
Admin releases the box – logged with the admin's name.
Your bike was unexpectedly removed from Stellplatz 1!
The box was not opened. The operator has been informed and is checking the station.
Got it – stop alarm
Acknowledging the message stops sound, vibration and blinking. The box stays blocked until an admin releases it.
Smart Bikestation · User journey
7

## Slide 8
THE ADMIN JOURNEY
Keeping an eye on every station
One page, ordered by urgency: who is where, what needs action, and the full history at the bottom.
1
Who is at which box?
Stellplatz 1 · Hackathon Halle Occupied by testfahrer · bike inside since 10:41 · Locked
2
Manage stations
Add a station (gets the next number = hardware slot_id), change its location, delete a free station.
3
Open alerts & blocked boxes
Tampering, AI anomalies, bike removed → resolve; blocked boxes → release after checking on site.
4
Box log (dropdown)
"testfahrer booked Stellplatz 1 (Hackathon Halle) on 29.09.2026 at 10:41:06 – latch opened." Filter by user.
Smart Bikestation · User journey
8

## Slide 9
DESIGN PRINCIPLES
Built in from the start
Privacy by design
No cameras. Accounts are username + password hash only. Sensor readings are deleted after 90 days. Other users' names are visible to admins only.
Accessible
Clear text instead of colour codes ("Stellplatz 1 is free"), keyboard and screen-reader friendly, light/dark mode, German, English and Dutch.
Safe by default
The server decides, the station executes. Only the owner opens a box. A blocked box stays closed until a human checks it.
Tested
61 automated tests cover booking, latch, alarm, permissions, timeouts, stations and the admin log.
Smart Bikestation · User journey
9

## Slide 10
UNDER THE HOOD
How the journey is powered
One rule keeps it simple: the station measures, the server decides, the app shows.
Station
Raspberry Pi 5 HC-SR04 ultrasonic Servo latch · green LED parking_sensor.py
↔
Server
ASP.NET Core 10 (C#) Box state machine SQLite · background jobs port 8080
↔
Web app
React + TypeScript User & admin pages refresh every 2–3 s DE · EN · NL
Station ↔ Server
Every second: POST /api/sensor-data {slotId, distance} with API key → answer {boxState, lockOpen}.
Server ↔ Web app
REST + JWT: book, cancel, pick up; admin: occupancy, stations, alerts, log.
States: Free → OpenForParking → Locked → OpenForPickup → Free · Locked → Blocked (alarm) → Free
Smart Bikestation · User journey
10

## Slide 11
WHAT'S NEXT
Improving the journey further
1
Alarm on the lock screen
HTTPS + Web Push, so the alarm reaches the phone even when the browser is closed.
2
More stations
Each new box just needs the same hardware and its number – the admin adds it in one click.
3
Second sensor
Weight sensor via ADS1115 as a second opinion next to ultrasonic.
4
Own server
Move from the Windows PC to Linux (Pi 5 / Proxmox) for 24/7 operation.
Smart Bikestation · Hackathon 2026 · Try it live at Stellplatz 1, Hackathon Halle